## Slide 1: Radar image reconstruction with raw ADC data
TingYing Chu

## Slide 2: Outline
Radar data processing
Literature review
Possible future works
Timetable

## Slide 3: Radar data processing
Data processing pipeline
  Input: ADC raw signal (4D)
  Output: Object detection information
    Range
    Doppler
    Azimuth
    elevation
py-core code
  Understanding the code with the pipeline
  Ran the code on PC
  Still setting the environment to run the code on the server
processing steps

## Slide 4: Literature review
Models
  ADCNet (2023):
    Outperform T-FFTRadNet
    Better performance on High Definition (HD) radar
  T-FFTRadNet (2023)
    Better performance on Low Definition (LD) radar
Public raw ADC Dataset (road)
  RADIal: HD radar data; Currently unavailable
  RADDet: LD radar data
End-to-end model with raw ADC radar data
ADCNet experiment on HD radar data
T-FFTRadNet experiment on HD radar data
T-FFTRadNet experiment on LD radar data

## Slide 5: Possible future works
Idea: Utilizing the technique of pre-training ADC to RAD via distillation
  Use our py-core to create RAD cube
    ADCNet use SDK algorithm for estimating AoA
    The paper mentioned that future work is having advanced algorithm (such as IAA, MUSIC)
Possible direction
  First, apply ADCNet on our dataset
  Second, adjust the model via changing the algorithm for creating RAD cube
  Third, try different backbone model
Based on ADCNet

## Slide 6: Timetable
Task | April |  |  |  | May |  |  |  | June |  |  |  | July |  |  |  | August |  |  |  | September |  |  |  | October |  |  | 
Understanding py-core code and data processing pipeline; Testing code with imec server |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Literature review and problem definition |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data collection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Model selection and implementation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Evaluation and Fine-tuning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Visualization and interpretability |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Thesis writing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gantt chart

## Slide 7: Appendix
Radar data pre-processing

## Slide 8: Radar data pre-processing
Range processing
  Applies an FFT over the sampling (4th ) dimension
Doppler processing
  Applies a 2nd FFT on the chirp loop (1st ) dimension
MIMO decoding & Equalization
Antenna mapping
  Map the physical to virtual
Beamforming
  applying FFT over the vertical and horizontal antenna dimensions, one can get elevation (vertical angle) and azimuth (horizontal angle)
Cube generation
Range processing
Doppler processing
Antenna mapping
Beamforming
  Chirp dimension
  Transmit antenna dimension
  Receive antenna dimension
  Range dimension
  Velocity dimension
  Transmit antenna dimension
  Receive antenna dimension
  Range dimension
  Velocity dimension
  Vertical antenna dimension
  Horizontal antenna dimension
  Range dimension
  Velocity dimension
  Elevation dimension
  Azimuth antenna dimension
  Range dimension
  Chirp dimension
  Transmit antenna dimension
  Receive antenna dimension
  Sampling dimension
  Raw ADC

## Slide 9: Radar data pre-processing
CFAR processing
  Detect targets in radar data cube (with threshold)
(2D) target extraction
  Grouped detections with a multi-dimensional centroiding algorithm
AoA processing
  Azimuth and elevation estimations for targets (using techniques, MUSIC algorithm, that more accurate than FFT)
(4D) target post-processing
  Single-target: reject weakest targets and keep the most prominent target
  Multiple-target: group detected targets based on distance
Multi-target tracking
  Estimate the tracks of the targets
Target detection steps

## Slide 10: Deep Learning Model
ADCNet: End-to-end perception with raw radar ADC data
FFT-RadNet
  Structure: MIMO pre-encoder+ encoder-decoder
ADCNet
  Structure: trainable DSP module (as pre-encoder) + encoder-decoder (FFT-RadNet)
Loss function
  Detection head: focal loss + smooth L1 loss
  Segmentation head: Binary cross-entropy loss
FFT-RadNet architecture
ADCNet architecture

## Slide 11: Deep Learning Model
T-FFTRadNet: Object Detection with Swin Transformers from Raw ADC Radar Signals
FFT-RadNet
  Structure: MIMO pre-encoder+ encoder-decoder
T-FFTRadNet
  Structure: transformation layer (as pre-encoder) + hierarchical Swin Transformer (as encoder) + encoder (FFT-RadNet)
Loss function
  Detection head: focal loss + smooth L1 loss
  Segmentation head: Binary cross-entropy loss
  T-FFTRadNet: Detection head (LD Radar): focal loss + smooth L1 loss + pixel-wise cross-entropy loss
FFT-RadNet architecture
T-FFTRadNet architecture
Transformation layer