## Slide 1: FFT-RadNet vs. conventional data preprocessing
TingYing Chu

## Slide 2: FFT-RadNet
MIMO Pre-encoder:
  Reorganizing and compressing the RD cube
Feature Pyramidal Network (FPN) encoder:
  Feature extraction
Range-Angle decoder:
  Building a range-azimuth latent representation
Detection head:
  Localizing vehicles in range-azimuth coordinates
  Predicting range and azimuth values
Segmentation head:
  Predicting the free driving space
Model structure
RD cube

## Slide 3: FFT-RadNet
Performs reorganization of the input tensor (range-doppler profile)
The pre-encoder organize and compress signatures in fewer than NTx·NRx output channels
  First layer: A convolution layer (gathering Tx and Rx information)
  Second layer: Second convolution layer (learns how to combine these channels and compresses the signal)
The role of the MIMO pre-encoder is to transform RD spectrum into a representation that is compact and still allows the prediction of azimuth angles along with other information
MIMO pre-encoder
MIMO pre-encoder
Notes: For each receiver, its signature will be visible NTx times, one per transmitter. More specifically,
First layer: first a suitably-defined Atrous convolution layer that gathers Tx and Rx information at the right positions.
Second layer: A second convolution layer, with a 3×3 kernel, learns how to combine these channels and compresses the signal.

## Slide 4: FFT-RadNet
FPN encoder
  Using a pyramidal structure to learn multi-scale features
  The role of FPN encoder is to extract feature maps from processed RD spectrum
Range-angle decoder
  Aims to expand the input feature maps to higher resolution representations
  This expansion is achieved through multiple deconvolution layers (output is combined with previous feature maps to preserve spatial details)
  The role of range-angle decoder is to output RA latent representation
FPN Encoder & Range-Angle decoder
Output from 2nd ResNet Block
Output from 3rd ResNet Block
Notes: Our FPN architecture uses 4 blocks composed of 3, 6, 6 and 3 residual layers [14] respectively
The channel dimensions are in fact chosen to encode at best the azimuth angle over the entire distance range (i.e., high resolution and narrow field of view at far range, low resolution and wider field of view at near range).
High resolution and narrow field of view at far range: At far distances, where objects are relatively distant from the radar sensor, it's crucial to have high resolution to accurately detect and distinguish objects, especially when the angular difference between objects may be small. Additionally, a narrow field of view helps focus the radar beam, allowing for more precise measurements over longer distances.
Low resolution and wider field of view at near range: Conversely, at closer distances, where objects are nearer to the radar sensor, the angular difference between objects tends to be larger. In this case, a wider field of view can cover a larger area, enabling the radar to capture more objects within its range. However, since objects are closer, the resolution requirements may not be as stringent as at far ranges.

## Slide 5: FFT-RadNet
Detection Head
  Classification pathways: predict the probability each “pixel” (range-azimuth coordinates) as occupied or not by a vehicle
  Regression pathways: finely predicts the range and azimuth values corresponding to the detected object
Segmentation Head
  Classification : predict the probability each “pixel” to be drivable
Detection Head
Notes: The deconvolution layers upscale only the range axis, producing feature maps that are concatenated with those from the previous pyramid level. A final block of two Conv-BatchNorm-ReLU layers is applied, generating the final range-azimuth latent representation.

## Slide 6: FFT-RadNet
Original dataset: RADIal dataset (currently not available, requesting data from authors)
Current solution: Using our MATLAB code (MATLAB-RADAR-AUTOMOTIVE) to simulate the input data
Input data
  Creating targets
  Using targets to generate data
  Take the RD cube before data going into MIMO processing
Output data
  Using targets to calculate the ground truth (labels)
Questions for input data:
  The input tensor dimension is 512*256,*32 (BR, BD, 2*NRx)
model implementation
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 7: Next steps
This week:
  Finish generating input and output data, matching with the model dimension and the paper explanation
    Input: Match the dimension and the structure of RD cube
    Output: Implement labels pre-processing
Nest week:
  Training and evaluating the model with our simulation dataset
  Compare the result with paper
model implementation
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 8: Timetable
Task | April |  |  |  | May |  |  |  | June |  |  |  | July |  |  |  | August |  |  |  | September |  |  |  | October |  |  | 
Understanding py-core code and data processing pipeline; Testing code with imec server |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FFT-RadNet implementation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data preparation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Literature review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Model selection and implementation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Evaluation and Fine-tuning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Visualization and interpretability |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Thesis writing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gantt chart

## Slide 9: Appendix
ADCNet & FFTRadNet

## Slide 10: ADCNet
Backbone: FFT-RadNet

## Slide 11: ADCNet
Learnable window
Learnable DFT

## Slide 12
Range and Doppler processing: range-doppler profile
Windowing function

## Slide 13: FFT-RadNet