## Slide 1: Radar image reconstruction with raw ADC data
TingYing Chu – Report 06

## Slide 2: MATLAB simulation dataset
Parameter setting
  Number of Tx: 12, Number of Rx: 16
  Number of targets: 1, 3
  Dataset size: 500 samples
Generation steps
  Randomly generate 1 or 3 targets per sample
  Use the randomly generated targets to generate RD cube
Two dataset for the FFTRadNet
  One target dataset
  Multi-targets dataset (3 targets)
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 3: FFTRadNet model
Parameter setting
  Number of epoch: 300, 500
  Batch size: 4
  Train-validation-test dataset: 70%-15%-15%
  Dataloader: no shuffle
Result
  The prediction result at previous meeting is not accurate
    The code for plotting misplace, so that the result is plotting by the model that is still updating the weights
  Adjust the plotting code to ensure the result comes from the final model
Implementation setting
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 4: FFT-RadNet
Model training prediction
Number of target = 1
Number of target = 3
Epoch=499
Epoch=150
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 5: FFT-RadNet
Evaluation score
  Calculated with the same training dataset
  Can’t calculate scores for validation dataset -> unable to check overfitting (explain in next slide)
Model training prediction
 | Number of target = 3 |  | Number of target = 1 | 
 | epoch:499 | Epoch:150 | epoch:499 | epoch:150
mAP | 0.964 | 0.543 | 0.867 | 0.435
mAR | 0.992 | 0.739 | 0.957 | 0.546
F1 score | 0.978 | 0.626 | 0.910 | 0.484
Loss (detection loss+ regression loss) | 1.6098 | 18.6216 | 4.9607 | 24.7359
Detection loss
regression loss
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 6: FFT-RadNet
Evaluation mode (nn.Module.eval())
  Create a consistent environment for model inference
  BatchNorm2d and Dropout behave differently on evaluation and training mode
  BatchNorm2d
    Training mode: use batch statistic
    Evaluation mode: uses the running estimates (mean and variance) that it computed during it's training phase
No evaluation score on train dataset with eval() & validation dataset without eval() -> unable to reproduce the performance on train dataset
  Tried solutions: BatchNorm layer: set running_stat=False (evaluation mode use batch statistic), shuffle training dataset, adjusting momentum value (more weights on new statistic, ex, 0.5) -> these methods didn’t solve the issue
Model evaluation
momentum
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 7: Next step
Increase the batch size, from 4 to 16 or more
  The author trained with sequential dataset, but we use random dataset -> might need bigger batch size
Implement the complex layer
Camera image for the RADIal dataset input
Three target: starting loss 17k
Complex layer
T-FFTRadNet
One target: starting loss 1200k
Epoch 150: loss 24.73
Epoch 500: loss under 10
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 8: Appendix

## Slide 9: FFT-RadNet
model implementation
Loss function
Dataset
  Original dataset: RADIal dataset (currently not available)
  Implementation dataset: Using our MATLAB code (MATLAB-RADAR-AUTOMOTIVE) to simulate the input data
Model:
  Input data: RD cube
  Output data
    Binary classification: each “pixel” (RA map) as occupied or not by a vehicle
    Regression: finely predicts the range and azimuth values corresponding to the detected object.
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth

## Slide 10: T-FFTRadNet
To deal with the special MIMO setting
Notes: Study the code for understanding the dimension of the input and output data
The author pre-processed their labels data, need to check how to match with our ground truth